NOTIFICATION TO AN AFFECTED PARTY OF A PROPOSED ACTIVITY

UNDER ARTICLE 3 OF THE CONVENTION

“The extension of a pig fattening farm” project, in Turnu village, Pecica city, Arad county, cadastre number 302335

| 1. INFORMATION ON THE PROPOSED ACTIVITY |
| --- |
| (i) Information on the nature of the proposed activity |
| Type of activity proposed: | Pig production |
| Is the proposed activity listed in Appendix I to the Convention? | The proposed activity is listed in Appendix I to the Convention, point 20 |
| Scope of proposed activity (e.g. main activity and any/all peripheral activities requiring assessment) | Pig fattening farm, capacity: 12500 places |
| Scale of proposed activity (e.g. size, production capacity, etc.) | Pig fattening farm, capacity: 12500 places; 5 barns of 2500 places each, manure storage tanks 8000 cubic meters, land area 36900 square meters |
| Description of proposed activity (e.g. technology used): | Pig fattening from 25-30 kg to 110 kg; fattening in closed system barns, mechanically ventilated barns, prefabricated concrete slabs flooring with slurry collected in underground pits that discharge into slurry storage tanks; maximum 3,4 series per year resulting in a production of 4675 tons/tear. Automatic feeding and watering |
| Description of purpose of proposed activity: | The main object of activity of the farm is the fattening of pigs from the weight of 25 kg to the slaughter weight (105-110 kg), in an intensive close circuit system |
| Rationale for proposed activity (e.g. socio-economic, physical geographic basis) | Capitalizing on the economic potential of the area |
| Additional information/comments | Additional information is provided in the Presentation Memoir, the air pollutant dispersion modelling study and Water impact assessment study. |
| (ii) Information on the spatial and temporal boundaries of the proposed activity |
| Location: | Turnu village, Pecica city, Arad county, cadastre number 302335, Romania Distance from the border with Hungary: 4,085 km |
| Description of the location (e.g. physical-geographic, socio-economic characteristics); | The land surface of 36900 square meters on documents (36217 sqm measured) is identified as follows: land book 302335, cadaster number 302335 (old cadaster no. 2908), located inside the build-up area of Pecica city, Arad county |
| Rationale for location of proposed activity (e.g. socio-economic, physical-geographic basis): | Land availability; great distance from inhabited areas |
| Time-frame for proposed activity (e.g.: start and duration of construction and operation) | The duration of the construction works is 12 months; the start date of the works is estimated to be: March 2021 Normal service life is: 25 years |
| Maps and other pictorial documents connected with the information on the proposed activity | They are presented in the attached documents: presentation memoir, pollutant dispersion study |
| Additional information/comments | Additional information is provided in the Presentation Memoir, the air pollutant dispersion modelling study and Water impact assessment study. |
| (iii) Information on expected environmental impacts and proposed mitigation measures |
| Scope of assessment (e.g. consideration of: cumulative impacts, sustainable development issues, impact of peripheral activities, etc.): | Possible cumulated impact with other similar farms in Arad County: in total there are 14 farms in operation and 3 farms in the project phase, to which is added this project |
| Expected environmental impacts of proposed activity (e.g. types, locations, magnitudes): | - Air emissions: NH3, dust (PM10, PM2.5), NOx - Manure - applied on agricultural land - Smells - are properly managed |
| Inputs (e.g. raw material, power sources, etc.) | The amount of raw materials and energy that will be needed to carry out the project: - Piglets for fattening: 1063 tons/year - Feed: 14600 tons/year - Drinking water: 45625 cbm/year - Pens wash water: 229 cbm/year - Materials for veterinary use: 18.75 tons/year - Diesel incinerator: 20 tons/year - Other materials: 18.75 tons/year Utilities required for construction work: - Electricity: 600 MWh/year (19-48 kWh/head/year) - Water required for staff: 0.75 cbm/day - Necessary water sanitation spaces: 0.613 cbm/day - Required water for biological consumption: 125 cbm/day - Total water required: 126,363 cbm/day or 46122.5 cbm/year - sewage waters - in drainable basin, max. 0.75 cbm/day - Washing water: max. 0.613 cbm/day - in slurry tanks - Rainwater: in the retention basin 100 m3 - Manure: 16474cbm/year-collected in basins of 8000cbm The water needed to carry out the project will be taken from an underground source During the operation of the farm, the water supply is made from an underground source For the power supply, the site organization will be connected to the network in the area Raw materials will be purchased from authorized Feed Factories Other information is presented in the presentation memoir. |
| Outputs (e.g. amounts and types of: discharges in air, discharges into the water system, solid waste) | The results of the air pollutant dispersion modelling study: The modelling was done in 3 scenarios: Scenario 1 - the situation without a project. The operation in Arad County of all existing animal farms that have an integrated environmental permit, to which are added the projects of animal farms that are in the approval procedure at Arad Environment Protection Agency and that have a high probability of being implemented; Scenario 2 - the situation with the project. Operation in Arad County of all existing animal farms that have an integrated environmental permit, to which are added the projects of animal farms that are in the process of approval at Arad Environment Protection Agency and that have a high probability of being implemented, as well as the project analysed. This will highlight the influence of the analysed project on air quality, in the context of the operation of all relevant and similar sources in Arad County. Scenario 3 - only the analysed project. In this scenario, only the emissions of the analysed project are taken into account. This highlights the absolute values ​​of the concentration of pollutants in the atmosphere, strictly emitted by the project. It also highlights the dispersion area of ​​these pollutants and potential receptors that may be influenced by farm emissions. Following the mathematical modelling, the following conclusions emerged: Authorized active farms and the 3 projects under regulation do not significantly influence air quality in terms of concentration in NH3, PM10, PM2.5 and NOx. At the border, air quality is very weakly influenced, mainly by the Macea Pig Breeding Complex, which is also closest to the border (approx. 4 km). For the analysed farm (VR ROM MEAT project) a dispersion wedge is distinguished from the other farms. Thus, the influence of the farm on the atmospheric air quality does not cumulate with the influence of the emissions of the other farms. The area of ​​influence of the analysed farm is a maximum of 3 km around it, without touching the border area. The calculated concentrations of pollutants in the atmospheric air are much lower than the maximum allowed. Thus, the influence of the proposed farm emissions on the neighbourhoods is very low in terms of NH3, PM10, PM2.5 and NOx pollutants. The population in the neighbouring settlements will not be significantly affected by the farm's ammonia emissions or other types of pollutants. The influence of the analysed project on the air quality in the Romania - Hungary border area is very low |
| Transboundary impacts (e.g. types, locations, magnitudes): | The cross-border impact on environmental factors is described: AIR: Following the mathematical modelling, the following conclusions emerged. Authorized active farms and the 3 projects under regulation do not significantly influence air quality in terms of concentration in NH3, PM10, PM2.5 and NOx. At the border, air quality is very weakly influenced, mainly by the Macea Pig Breeding Complex, which is also closest to the border (approx. 4 km). For the analysed farm (VR ROM MEAT project) a dispersion breakdown is distinguished from the other farms. Thus, the influence of the farm on the atmospheric air quality does not cumulate with the influence of the emissions of the other farms. The area of ​​influence of the analysed farm is a maximum of 3 km around it, without touching the border area. The calculated concentrations of pollutants in the atmospheric air are much lower than the maximum allowed. Thus, the influence of the proposed farm emissions on the neighbourhoods is very low in terms of NH3, PM10, PM2.5 and NOx pollutants. The population in the neighbouring settlements will not be significantly affected by the farm's ammonia emissions or other types of pollutants. Other environmental factors: • The project has no transboundary impact on other environmental factors |
| Proposed mitigation measures (e.g. if known, mitigation measures to prevent, eliminate, minimize, compensate for environmental effects): | During execution - measures to prevent dust emissions into the atmosphere and to prevent leaks; measures for the correct management of the resulting waste; During operation: adoption of BAT techniques for pig fattening activity; proper manure management, proper wastewater management; waste management etc. |
| Additional information/comments | The project was submitted to the procedure of obtaining the Water Management Permit with Water impact assessment study |
| Name, address, telephone and fax numbers | Beneficiary: S.C. VR ROM MEAT S.R.L. Address: Bucharest, sector no. 2, Zece Mese street, no. 7, stair A, room 11, ap.1; C.U.I. 30421389; J40/8076/11.07.2012 Phone: +40743552313 Fax: - E-mail: econova_iasi@yahoo.com Website address: - |
| (v) EIA documentation |
| Is the EIA documentation (e.g. EIA report or EIS) included in the notification? | NO |
| If no/partially, description of additional documentation to be forwarded and (approximate) date(s) when documentation will be available | The notification includes: - Presentation memoir - Study of dispersion of pollutants in the atmosphere; The EIA report will be available after the completion of the classification stage and the stage of defining the evaluation area in the EIA procedure. |
| Additional information/comments |  |
| 2. POINTS OF CONTACT |
| (i)Point of contact for the possible affected Part or Parties: |
| Authority responsible for coordinating activities relating to the EIA (refer to decision I/3, appendix): Name, address, tel and fax numbers | Ministry of Agriculture of Hungary Ms. Virág POMOZI Adviser Department of Environmental Preservation Apáczai Csere János u. 9. 1051 BUDAPEST Telephone: +36 1 795 6131 E-mail: virag.pomozi(at)am.gov.hu |
| List of affected parties to which notification is being sent | Hungary |
| (ii) Points of contact for the Party of origin |
| Authority responsible for coordinating activities relating to the EIA ( refer to Decision I/3, appendix) Name, address, tel and fax numbers | Ministry of Environment, Waters and Forests Ms. Dorina MOCANU Director Directorate for Impact Assessment and Pollution Control Liberty Boulevard, no. 12, sector 5, Bucharest, Romania – 040129 Telephone: 004021/4089588 Fax: 004021/3160421 |
| Decision making authority if different than authority responsible for coordination activities relating to the EIA Name, address, tel and fax numbers | Arad Environment Protection Agency Address: Splaiul Mureșului, FN, Arad City, Arad County Telephone: 0257-280996; 0257-280331 Fax: 0257-284767 e-mail: office@apmar.anpm.ro |
| 3. INFORMATION ON THE EIA PROCESS IN THE COUNTRY WHERE THE PROPOSED ACTIVITY IS LOCATED |
| (i) Information on the EIA process that will be applied to the proposed activity: |
| Time schedule: |  |
| Opportunities for the affected party/parties to be involved in the EIA process | Yes. Hungary may decide to participate in the environmental impact assessment procedure and respond to the notification by 22.02.2021. |
| Opportunities for the affected party/parties to review and comment on the notification and the EIA documentation | Yes. Comments and requirements for the scoping document are expected by 08.03.2021. Hungary is also invited to send information relating to the potentially affected environment under its jurisdiction, so that the information can be used for the preparation of the EIA documentation. |
| Nature and timing of the possible decision: | EIA decision to be issued during this year. |
| Process for approval of the proposed activity | In Romania, the EIA procedure is conducted according with the Law no. 292/3018 on environmental impact assessment of certain public and private projects. The EIA procedure comprises participation of the Romanian authorities and public, and also the participation of the likely affected Party’s authorities and public. |
| Additional information/comments |  |
| 4. INFORMATION ON THE PUBLIC PARTICIPATION PROCESS IN THE COUNTRY OF ORIGIN |
| Public participation procedures |  |
| Expected start and duration of public consultation | When a project is likely to affect the environment of another Party, the national competent authority for environmental protection notifies the potentially affected Party, as early as possible. Then, the environmental authority from the affected Party informs its own public from the potentially affected areas and its concerned authorities. In 6 weeks from sending the notification, the Party of origin expects from the affected Party the summary of its public’s and competent authorities‛ comments, in English. The scoping document will include the requests sent by the affected Party, as a response to the notification. After its elaboration, the EIA documentation is made available to the public, which is given 30 days to express its opinion. The EIA documentation is also sent to the affected Parties, which then send their public’s and competent authorities‛ comments, in English, to the Party of origin. A public hearing is organized in the area of the project. If the affected Party finds it necessary, a public hearing is held on its territory, as well. The final EIA decision takes into consideration the comments received from the affected Party the same way as those of the national public and authorities. |
| Additional information/comments |  |
| 5. DEADLINE FOR RESPONSE |
| Date | 22.02.2021 |